## Slide 1: TCP/IP MODEL

## Slide 2: TCP/IP PROTOCOL SUITE
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model.
The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application.
However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.

## Slide 3: TCP/IP Protocol Suite
The TCP/IP protocol suite is a hierarchical protocol , made of five layers:
  Physical layer
  Data link layer
  Network layer
  Transport layer
  Application layer.

## Slide 4: TCP/IP Protocol Suite
The term hierarchical means that each upper-level protocol is supported by one or more lower-level protocols.
TCP/IP protocol suite contain relatively independent protocols that can be mixed and matched depending on the needs of the system.

## Slide 5: TCP/IP Model
TCP/IP Model
Application Layer
Application programs using the network
Transport Layer (TCP/UDP)
Management of end-to-end message transmission,
error detection and error correction
Network Layer (IP)
Handling of datagrams : routing and congestion
Data Link Layer
Management of cost effective and reliable data delivery,
access to physical networks
Physical Layer
Physical Media

## Slide 6: OSI & TCP/IP Models
TCP/IP Model

## Slide 7
PROTOCOLS IN TCP/IP and OSI model

## Slide 8
TCP/IP and the OSI Model

## Slide 9: IP PROTOCOL
Transmission mechanism used by the TCP/IP protocols.
Unreliable and connectionless protocol-a best-effort delivery service.
The term best effort means that IP provides no error checking or tracking.
Best-effort means that datagrams may:
– be lost;
– arrive out of order;
– even be duplicated.
IP transports data in packets called datagram, each of which is transported separately.

## Slide 10: FOUR supporting protocols
ARP
RARP
ICMP
IGMP

## Slide 11: Address Resolution Protocol(ARP)
The Address Resolution Protocol (ARP) is used to associate a logical address with a physical address.
On a typical physical network, such as a LAN, each device on a link is identified by a physical or station address, usually imprinted on the network interface card (NIC).
ARP is used to find the physical address of the node when its Internet address is known.

## Slide 12
Figure 24-13
ARP

## Slide 13: Reverse Address Resolution Protocol
The Reverse Address Resolution Protocol (RARP) allows a host to discover its Internet address when it knows only its physical address.
It is used when a computer is connected to a network for the first time or when a diskless computer is booted.

## Slide 14: ICMP & IGMP
Internet Control Message Protocol:
  A mechanism used by hosts and gateways to send notification of datagram problems back to the sender.
  Sends query and error reporting messages.
Internet Group Message Protocol:
  Used to facilitate the simultaneous transmission of a message to a group of recipients.

## Slide 15: TRANSPORT layer protocols
UDP
TCP
SCTP

## Slide 16: User Datagram Protocol
The User Datagram Protocol (UDP) is the simpler of the two standard TCP/IP transport protocols.
A process-to-process protocol that adds only port addresses, checksum error control and length information to the data from the upper layer.

## Slide 17: Transmission Control Protocol
The Transmission Control Protocol (TCP) provides full transport-layer services to applications.
Reliable stream transport protocol.
Stream  Connection-oriented: A connection must be established between both ends of a transmission before either can transmit data.
Sending end :
  TCP divides a stream of data into smaller units called segments.
  Each segment includes a sequence number for reordering after receipt, together with an acknowledgment number for the segments received.
  Segments are carried across the internet inside of IP datagrams.
Receiving end:
TCP collects each datagram as it comes in and reorders the transmission based on sequence numbers.

## Slide 18: Stream Control Transmission Protocol (SCTP)
The Stream Control Transmission Protocol (SCTP) provides support for newer applications such as voice over the Internet. (VoIP)
VoIP - a category of hardware and software that enables people to use the Internet as the transmission medium for telephone calls by sending voice data in packets using IP
It is a transport layer protocol that combines
the best features of UDP and TCP.

## Slide 19: ADDRESSING
Four levels of addresses are used in an internet employing the TCP/IP protocols:
  Physical address
  Logical address
  Port address and
  Specific address.

## Slide 20
DEVICES :
Hub: A distributor that has a lot of ports which connected to computers.
Switches: Like a hub but it transmit packets to it destination
Bridge: Used to connect two similar LANs.
Routers: Choose the best path to transmit the packet.
Gateway: Used to connect two different LANs and connect different application protocols.
Repeaters: Repeats signals that travels via long distance

## Slide 21: Some Protocols in TCP/IP Suite